## Slide 1: Digital Image Processing with CUDA
By Abdoula Barry, CSYS
Advanced Computer Systems; Fall 2023

## Slide 2: Overview
CUDA Introduction and Basics
Applications in Image Processing
Gaussian Blur
Results
Host vs Device Performance
Future Improvements and Additions
Lessons Learned

## Slide 3: Compute unified device architecture (Cuda)
Introduced in November 2006 by NVIDIA
General Purpose Parallel Computing Platform
Hides GPU HW from developers
3 key abstractions
  A hierarchy of thread groups
  Shared Memories
  Barrier Synchronization

## Slide 4: CUDA programming model
Work distributors forward stream to Streaming Processor Array
Streaming Multiprocessors execute parallel computing programs
Shared Memory holds shared data between Streaming Processors for thread communication

## Slide 5: CUDA Programming model
Parses Source -> Creates 2 files : host and device
Host – CPU
Device – GPU
CUDA object files written in PTX, the CUDA instruction set architecture

## Slide 6: CUDA Programming model
Serial Code executes on host
Parallel Code on device

## Slide 7: Applications in image processing
Image processing is a natural fit for parallel processing
Pixels mapped directly to threads
Each thread can write more than one pixel
Applications
  Convolutions
  Image & Video Compression
  Noise Reduction
  Histograms

## Slide 8: Gaussian blur
Image smoothing to reduce noise and detail
Low-pass filter
Reduces disparity between pixels by nearby ones
Less weight to pixels further from center of window

## Slide 9: results
Original Image
Altered Image

## Slide 10: Host vs device performance
Chart: Gaussian Blur (GPU vs CPU)
| 512x512 | 1024x768 | 1920x1080 | 2560x1280 | 3200x2400
GPU | 0.4 | 0.7 | 1.4 | 2.6 | 8.3
CPU | 8.44 | 25.23 | 75.19 | 108.77 | 324.57

## Slide 11: Information learned and topics to explore
SIMT – Single Instruction Multiple Thread
  -SIMT instruction unit subdivides threads into groups of 32 called warps
  -Warp allows for thread scheduling in a Streaming Multiprocessor
SPMD – Single Program Multiple Data : widely used in parallel computing systems
  -Asynchronous version of SIMD
Sobel Edge Detection
Explore Video Processing with CUDA
Object Recognition

## Slide 12: GPU Architecture